## Slide 1: Hydrogen Transportation - Advancing Type V Technology for Efficient Sustainable Distribution
« ROAD TRHYP » ROAD trailer design – use of Type V theRmoplastic tube with light composite structure for HYdrogen transPort
2023 - 2025

## Slide 2: Content
Origin of the project / Main objectives
Approach
Achievements :
                Cylinder
                Safety
LCA
Conclusion & Perspectives

## Slide 3: Origin of the project
300 kg gH2
900 kg gH2
300 bar tube trailer
1,5 T gH2
Main objectives
Design Type V tubes according to EN17339
Elaborate a decontamination methodology to ensure H2 purity
Demonstrate the safety of Type V tubes
Demonstrate that a trailer made with Type V tubes will achieve 700 bar, 400 €/kg H2, 5,3 % H2 & improved environmental impact
Regulations aiming at faster deployment of the technology

## Slide 4: Approach and Objectives
Approach : design of MEGC based on a safety basis, develop the optimum composite cylinder to meet the max load on the road
Optimum cylinder Working Pressure to meet the 1,5 T in a gH2 trailer
Complying with usages
    To be able to dry / decontaminate the cylinder & trailer
    Collapse & Blister resistant
    To be compatible with gH2
5 ppm + ISO 14687

## Slide 5: High performance cylinder : Type V
Develop a thermoplastic composite cylinder with a monolithic structure C/PA11(*)
Monolithic cylinder structure :
- less assembly arrangement compared to Type IV
- the ability to do vacuum and improved drying / decontamination (DoE)
- increase the inner cylinder volume
Cylinder design :
- dome designed to remove most of liquid water after cylinder pressure test
Recyclability :
- 100 % recyclable
(*) PA11 100% biosourced

## Slide 6: Operate the cylinder in Europe & Comply with safety requirements
Transportation
Hydrogen refuelling station
Hydrogen cylinders & ancillary components
Regulations :
Dangerous goods: international
Pressurized gas transportation: national
Road vehicle weight & dimensions: national
Standards on transportable gas cylinder
Regulations :
Environment protection : national
Standards :
HRS design
Standards :
Ancillary components
Gas cylinders
Regulations are mandatory / Standards are voluntary.
Regulations are international and declined by country.
Notes: Faire prendre conscience que c’est pas simple et que les législations soient un match pour tous les pays européens.

## Slide 7: Trailer Safety Analysis
3 main accidental scenarios feared, leading to release of hydrogen : hose rupture, leakage on filling hose or pipings
Case no mitigation system is implemented : assessment of the severity of H2 flammable cloud ignition consequences (jet fire, explosion) → use of simple engineering models
CFD simulations planned in 2024 for
evaluation of the safety barriers

## Slide 8: Life Cycle Analysis

## Slide 9: Conclusion & Perspectives
Trailer Design to optimise tube working pressure to maximise the amount of gH2 in the trailer
Promising performances of Thermoplastic Type V cylinder (usages, performances)
Compliance with European regulation, Codes and Standards
Design to safety approach
Next to come :
Key performance tests for cylinders
Finalise trailer design → Working Pressure
Tank comportment in a hostile environment : fire
Key usage tests : decontamination & filling/unfilling
LCA : Type V trailer

## Slide 11: T5.3: Laboratory scale: mechanical behaviour of tanks exposed to fire
[M16-M36]
Task leader: PPRIME
Participants: COVESS, EFECTIS
Main objectives of this task are to :
  A/ Perform lab scale tests
    On samples cut or manufactured by COVESS
    To determine the mechanical behaviour at different temperatures and after fire exposure
  B/ Evaluate the inputs of different thermomechanical models
    Together with pyrolysis models from WP2
    To predicting variation of stiffness and strength of the composite material with temperature
  C/ Simulate the time-to-burst of a set of tubes representative of a module in a fire